## Slide 1: From NDT to SHM A Practical Approach
Holger Speckmann
Managing Director, Testia GmbH, Germany

## Slide 2: Content
TESTIA
NDT - SHM
Applications & Solutions
Use in Service – MSG3
Testia support along the process chain

## Slide 3: Content
TESTIA
NDT - SHM
Applications & Solutions
Use in Service – MSG3
Testia support along the process chain

## Slide 5: Content
TESTIA
NDT - SHM
Applications & Solutions
Use in Service – MSG3
Testia support along the process chain

## Slide 6: What is NDT?
In-Service
Nondestructive testing or non-destructive testing (NDT) is a wide group of analysis techniques used in science and technology industry to evaluate the properties of a material, component or system without causing damage
Equipment (sensors) cover a wide range of different applications
Active system (usually excitation/measurement in one unit/equipment)
Usually time consuming
Damages in hidden structures can only be inspected through other structures
Detectable damage size often increase with the thickness of the structure
Human interaction necessary
Only scheduled inspection possible
Mainly single, separated locations
To get access, removing of installations sometimes necessary
Source: Wikipedia

## Slide 7: Sections of the NDT Process
NDT/NDI ‚Non Destructive Testing / Investigation of materials and compounds with regard to defects, physical & chemical properties‘
Excitation
Probe X
Thermal
Mechanical
Magnetic
Electric
Electro-magnetic
Radiative (+ VIS)
Information on
Defects
Properties
Principle
Evaluation
Material, Compound
! Coupling ! Access
! Complex Interaction
! Processing ! Modelling
Interaction
Matter
Defects
Boundary Layers
Response
! Coupling ! Access ! Parasitic Effects
Detected Signal
Thermal
Mechanical
Magnetic
Electric
Electro-magnetic
Radiative (+ VIS)

## Slide 8: What is SHM?
SHM is the continuous, autonomous in-service monitoring of the physical condition of a structure by means of embedded or attached sensors with a minimum manual intervention, to monitor the structural integrity of the aircraft.
SHM system: monitoring of airframe and evaluation of the follow up maintenance actions
Human nervous system: detection of intensity and location of pain and doctor visit judgement
Evaluation
Notes:   +Guaranteed performance packages (measurements times) – WW SLA ?
+ skywise interface?

## Slide 9: The Global Approach
Use of real-time diagnostics (On-Condition maintenance)
Prognostics will avoid unnecessary unscheduled maintenance
No physical access required
Shorter inspection time
Less scheduled and unscheduled maintenance
A structural status communication
Cost Savings trend
Unscheduled
Costs
Time
Unscheduled
(Today)
Predictive
Scheduled

## Slide 10: SHM = Complexity
SHM is not
only a sensor

## Slide 11: SHM – Transdisciplinary Approach
Material+ Structure
Effects of defects (EOD)
Failures/Properties to be monitored
Determination of SHM method
Sensors
Reliability:
  Probability of Detection (POD)
  Durability
Application of sensors:
Modelling of optimised sensors placement
Simulation : -Bonding -Embedding
Data Transfer
Sensor/SHM Unit
SHM equipment:
Offboard
Onboard
Power Supply
Prognostic
Implementation
Manufacturing
Metals:
Corrosion
Fatigue
Composites:
Impacts
Overloads
BVID (Barely visible impact damage)
Debondings
Benefits:
DMC reduction
Increase availability
Postpone repairs
Data analysis
Diagnostic
Use for Maintenance
optimisation
Use for Design
optimisation
Benefits:
Reduction of Weight
Detection of Loads/Overloads

## Slide 12: What to detect or measure?
Measurement of in flight real A/C constrains
  Analysis of repercussion (ex: hard landing, tail bumper)
  Recording of exceptional, aerodynamic loads/strains
  Recording of loads in hot spot areas
  Customisation of A/C life cycle
  Flight control coupling for limitation of in flight constraints
Detection of damages
  Inspection in hazardous areas without direct access
  Weight saving through sizing cases deletion (e.g. broken stringer)
Monitoring of damage propagation:
  Postpone repairs to planned checks
  Reduction of downtime – Increased availability
Approach:
Multi Disciplinary approach:
  System compatibility, Cabin, Costumer support, Maintainability

## Slide 13: Benefits of SHM
SHM
Reduction of inspection time
Deferred maintenance / repair
Maintenance on demand
Reduced DOC, DMC
Increased Availability
Maintenance / Operatability
Design
Optimised structural efficiency
New design philosophies
Weight saving
Continuous and autonomous monitoring of defects, stress/strain, environmental and flight parameters by means of permanently attached or embedded sensor systems in order to ensure the structural integrity.

## Slide 14: Benefit of SHM
Scheduled Maintenance Process
Maintenance Plan
Document (MPD)
Aicraft Maintenance
Manual (AMM)
Not impacted
Possible Benefits
on
Performance of
inspection tasks
Non-destructive
Testing Manual (NTM)
Visual
Inspection time
&
procedures
process
Unscheduled Maintenance Process
Damage
assessment
tasks & Repair
decision
Possible Benefits
on
Damage
Inspection time
of temporary
repairs
EASA/FAA rules
Structure Repair
Manual (SRM) –
Service Bulletin
Repair Approval
Sheet (RAS) –
Additional damage
For Service Bulletins (Inspection and Mod), the process is similar

## Slide 15: 3rd Option for Service Bulletins
Damage detection in metal and composite structures to replace ISBs by SHM
Benefits:
  Avoiding development of complex NDT technology and complex description in NTM benefit for OEM
  Avoiding of penalizing inspections and opening areas with difficult access (100% of aircraft to be inspected, number of expected damages is only a few %) benefit for operator
  Use of SHM standard equipment, to be performed by non-specialist benefit for operator

## Slide 16: New, SHM enabled Design
s
Maintenance Interval
Maintenance benefit
Design benefit
Conventional (without SHM)
New design (SHM enabled)
SHM can provide a design benefit (weight saving) or a maintenance benefit

## Slide 17: Content
TESTIA
NDT - SHM
Applications & Solutions
SHM in Maintenance – MSG3
Testia support along the process chain

## Slide 18: Basic Maintenance Definitions & History
Maintenance as defined by World Airlines Technical Operations Glossary (WATOG*)
*today replaced by ATA Common Support Data Dictionary
Scheduled or Preventive Maintenance
That maintenance performed at defined intervals to retain an item in a serviceable condition by systematic inspection, detection, replacement of wear-out items, adjustment, calibration, cleaning, etc.
Unscheduled or Corrective Maintenance
That maintenance performed to restore an item to a satisfactory condition by providing correction of a known or suspected malfunction and/or defect

## Slide 19: MSG-3 & Maintenance Review Board Process
MSG-3 Document Evolution
Notes: The Maintenance Steering Group 3 (MSG-3) methodology for development of air carrier maintenance requirements continues to stand the test of time for almost 30 years past
Originally developed for large transport category aircraft, MSG-3 use is expanding worldwide to include regional and corporate aircraft, and recently helicopters
HISTORY
In July, 1968, representatives of various airlines developed Handbook MSG-1, "Maintenance Evaluation and Program Development," which included decision logic and inter-airline/manufacturer procedures for developing scheduled maintenance for the new Boeing 747 aircraft.
"Airline/ Manufacturer Maintenance Program Planning Document," MSG-2. MSG-2 decision logic was used to develop scheduled maintenance for the aircraft of the 1970's.
In 1979 experience and events indicated that an update of MSG procedures was both timely and opportune in order for the document to be used to develop maintenance for new aircraft, systems or powerplants. MSG3 was established.
The MSG-3 logic is task-oriented and not maintenance process oriented like the precedessor MSG-2. This eliminated the confusion associated with the various interpretations of Condition Monitoring, (CM), On-Condition (OC), Hardtime (HT) and the difficulties encountered when attempting to determine what maintenance was being accomplished on an item that carried one of the process labels.
MSG3 (Source: MSG3 document)
Airline and manufacturer experience in developing scheduled maintenance for new aircraft has shown that more efficient programs can be developed through the use of logical decision processes. These logical decision processes are covered by the MSG3 document.
MSG-3 adjusted the decision logic flow paths to provide a more rational procedure for task definition and a more straightforward and linear progression through the decision logic.
Structures logic evolved into a form which more directly assessed the possibility of structural deterioration processes. Considerations of fatigue, corrosion, accidental damage, age exploration and others, were incorporated into the logic diagram and were routinely considered.

## Slide 20: MSG3 preparation process
International Maintenance Review Board Policy Board
(IMRBPB)
Maintenance Program Industry Group
(MPIG, Facilitated by ATA)
Structural Health Monitoring Working Group
(SHMWG; Facilitated by ATA)
Draft IP
Candidate IP
MSG-3 Document
(Facilitated by ATA)
IP
Rework Loop (if needed)
Preparation Loop
The MPIG delegates the preparation of Issue Papers associated with
extensive MSG-3 revision proposal to dedicated working groups
(i.e. L/HIRF, SHM...)

## Slide 21: MSG-3 Document Revision Process
who is the “ATA MSG-3 SHM WG?”
Supporting the IP draft process with their advise
Notes: IMRBPB members:
  Federal Aviation Administration (FAA)
  Transport Canada Civil Aviation (TCCA)
  European Aviation Safety Agency (EASA)
  Hong Kong Civil Aviation Department (CAD)
  National Civil Aviation Agency – Brazil (ANAC)
  Civil Aviation Safety Authority Australia (CASA)
IMRBPB Charter:
(§6) The IMRBPB will only discuss issues related to the MRB/MSG process
(§6) IMRBPB reference documents:
  FAA Advisory Circular AC 121-2
  JAA Administration and Guidance Material (AGM), Maintenance Procedures Chapter 16
  TCCA TP 13850
(§8) Reference “IMRBPB Issue Paper management procedure”:
  IP to be submitted to IMRBPB chair 60 prior to scheduled IMRBPB meeting

## Slide 22: MSG-3 Document Revision Process
The Industry!
who is the “MPIG”?
Notes: MPIG CHARTER
MPIG is a self chartered organization within the disciplines of air carrier maintenance operations and air transportation manufacturers; facilitated by staff of the Air Transport Association (ATA) of America
MPIG represents the major air carrier operators, and manufacturers in developing consensus positions on regulatory proposals, emerging issues, maintaining the integrity of the ATA’s MSG-3 document, and proposing industry solutions
MPIG MISSION
Provide the industry with a forum of technical personnel experienced in the development of, management of, and revision to routine scheduled aircraft maintenance programs; a forum to propose resolution of associated issues in the best interests of the global air carrier industry, but with an overriding commitment to safety, airworthiness, legal fitness, reliability, and cost efficiency
MPIG VISION
Respond to air carrier maintenance-related needs, directives, and requests of the air transportation industry
Provide a forum for the discussion, proposed resolution, and settlement of issues arising from the Mission and to the needs and actions of regulatory authorities
MEMBERSHIP
  Each voting member of the MPIG shall be an employee of a certificated air carrier or an air transportation industry manufacturer or industry-supporting company
  Regulatory authorities are encouraged and welcome to attend, observe, and advise at MPIG meetings.
MEETINGS
  Unless required by circumstances, the MPIG shall conduct no more than two (2) face-to-face meetings each year; one during the 1st calendar year quarter (to include MPIG elections), and one during the 3rd calendar year quarter (in co-ordination with the annual meeting of the IMRBPB)
  A conscious effort is made to conduct any additional meetings via teleconference

## Slide 23: MSG-3 Document Revision Process
The Regulators!
who is the “IMRBPB?”
Notes: IMRBPB Charter
  IMRBPB is a system for the continued development of policies, procedures and guidance for the use of personnel operating under the purview of various Maintenance Review Boards (MRB’s)
  In addition to promoting harmonization with other regulatory authorities, the IMRBPB advocates the standardization of MRB policy and procedures
  The IMRBPB also provides a structured forum for discussions leading to the development of national and international policy regarding all MRB activities
IMRBPB members:
  Federal Aviation Administration (FAA)
  Transport Canada Civil Aviation (TCCA)
  European Aviation Safety Agency (EASA)
  Hong Kong Civil Aviation Department (CAD)
  National Civil Aviation Agency – Brazil (ANAC)
  Civil Aviation Safety Authority Australia (CASA)
IMRBPB Charter:
(§6) The IMRBPB will only discuss issues related to the MRB/MSG process
(§6) IMRBPB reference documents:
  FAA Advisory Circular AC 121-2
  JAA Administration and Guidance Material (AGM), Maintenance Procedures Chapter 16
  TCCA TP 13850
(§8) Reference “IMRBPB Issue Paper management procedure”:
  IP to be submitted to IMRBPB chair 60 prior to scheduled IMRBPB meeting

## Slide 24: MSG 3 Revision
The term S-SHM is introduced as a maintenance task level in MSG-3:
Scheduled SHM (S-SHM):
S-SHM is the act to use/run/read out a SHM device at an interval set at a fixed schedule
Structure inspection tasks for Accidental Damage (AD), Environmental Deterioration (ED) and /or Fatigue Damage (FD) can be replaced by a scheduled interaction with a SHM device where demonstrated to be applicable and effective
The structure section is revised to select S-SHM tasks and interval in lieu of classic inspections

## Slide 25: Inpection level according to MSG3, as of today
1. Visual Inspection
GVI (General Visual)
DET (Detailed)
Steered by MPD
Performed in according to AMM, etc.
2. NDT (Non Destructive Testing)
SDET (Special Detailed)
Using of Tools and equipment
Procedures mainly in NTM
Steered by MPD, SB, etc.
3. SHM
SDET (alternative to NDT)
Permanent installed sensors
Procedures for Off-Board use in NTM
On-Board and/or On-Line use via IVHM architecture “Automated SHM”

## Slide 26: SHM in MSG-3 IP105 (pending since 2010)
SHM Technology Type
In this respect two further scheduled maintenance SHM classification categories have been defined:
The MSG-3 principle concept avoids reference to specific (SHM) technology details as it should cater for the full range of application scenarios
SHM Operation Mode
  Scheduled SHM (S-SHM) – from IP92, no change
  Automated SHM - SHM technology which does not have a pre-determined interval at which maintenance action much takes place, but instead relies on the system to inform maintenance personnel that action must take place
  Damage Monitoring System – SHM technology that uses sensors to directly monitor structure for deterioration conditions
  Operation Monitoring System – SHM technology that uses sensors which do not directly check the structure for damage, but instead correlate various measurements (e.g. environment conditions, loads) to make an inference to the probability or likelihood of damage

## Slide 27: Content
TESTIA
NDT - SHM
Applications & Solutions
SHM in Maintenance – MSG3
Testia support along the process chain

## Slide 28: Application at In-Service – some examples
Structural Health Monitoring (SHM)
METALS
Crack detection
Crack growth monitoring
Corrosion detection
COMPOSITES
Impact detection and localisation
Repair monitoring
Delamination detection
Debonding
Sensors permanently applied on the structure
Fast automated inspection
No „physical“ access necessary
Continuously monitoring of known flaws
Inspection outside the maintenance schedule
Example: CVM
Example: Acousto Ultrasonics

## Slide 29: Maintenance Application
Fatigue Cracks
Damages caused
by corrosion
Inspection of Hidden areas without
removal of installations

## Slide 30: Examples of damage and load sensing technologies
A large scope of sensing technologies:
  CVM (Comparative Vacuum Sensors)
  Acoustic Emission
  Foil eddy current sensors
  Acousto Ultrasonic
  Fibre Bragg Gratings (FBG)
  …

## Slide 31: Content
TESTIA
NDT - SHM
Applications & Solutions
SHM in Maintenance – MSG3
Testia support along the process chain

## Slide 32: Testia support along the Process Chain
Installation
  Install sensors, cables, connectors, etc.
  All kind of sensors to be installed
  Worldwide service
  Service for all industries & all customers
Documents
  Develop and prepare documents for installation, instrumentation and protection
  Work in close cooperation with OEM, operators and authorities
Consultancy
  Act as focal point for all involved parties
  Make the link between OEM, system integrator and operator
  Expert in SHM Toolbox application
‘SHM Toolbox’

## Slide 33: Testia support along the Process Chain
Functional Check
  Perform functional checks of the system
  Certify performance
  Calibration & recalibration of systems
System Operation
  Being in-situ to perform the measurements
  Using tools to remote analyze areas with sensors
  Frequently reporting to customers
Protection
  Protect all SHM elements according to OEM needs

## Slide 34: Testia support along the Process Chain
Analysis
  Collect and store data (if requested)
  Evaluate data
  Diagnostic of data
  Simulation
Predictive Maintenance
  Use analyzed data to support prediction of failures
  Provide predictive maintenance solutions (Big Data analysis)
  End-to-End Life-Time-Monitoring
soperational
sstructure
Health Monitoring (HM)
Conventional Inspection (CI)
Maintenance Benefit
I HM
I CI
Interval
Repair & Maintenance
  Repair sensors, cables, connectors, etc.
  Reinstall sensors and protect
  Periodically check of sensor and equipment function

## Slide 35: Testia support along the Process Chain
Customer
  All Aerospace OEM
  Airlines, MRO, …….
  Other industries (construction, automotive, wind, ……)
Training
  Perform trainings for installation and operation of sensor systems
  eLearning for remote training & education
  Hands-On trainings for all sensor types
Supplier & Partner
  Provide the „Tool Box“ with the right technology for the right application
  Be a partner for SHM technology developer
‘SHM Toolbox’

## Slide 36: Testia could be your enabler of your regional policy
  Perform locally all SHM relevant Services
  Analyze and evaluate data in selected data analytic centers
Your local SHM workforce
Engineer & deliver your regional innovation initiatives & services
v
2019
2018
2019/2020
2020

## Slide 37: Thank you for your attention www.testia.com