## Slide 1: FAA Structural Health Monitoring SHM
Airlines for America NDT Forum
Paul Swindell
19 September 2018

## Slide 2: Outline
Past
Present
Future
Conclusion

## Slide 3
Paving the Path for SHM Innovation
Building the Infrastructure
SHM programs & guidance
End User
FAA

## Slide 4: Past
Why does the FAA care about SHM?
Transport Standards Branch (Transport Aircraft Directorate)
  Certification Issues
FY11 with AANC
Started with survey, review of SHM capabilities, gap analysis
Perform a mock certification

## Slide 5: Past-Emerging Technologies
Objective: Partner with the AANC, Delta Air Lines, SMS/AEM and Boeing to conduct trial SHM certification & integration activity
Application: Boeing737 NG Wing Box fitting cracking problem as application Boeing issued a service bulletin as a result of cracking after 21k cycles
Accomplishments:
  Install on Delta’s 737-700 Fleet going thru Atlanta for 5 ½ day checks (6k cycles)
  7 aircraft completed in Feb/March 2014
  Delta collected CVM data every 90 days as well as performing required NDI inspection
  Boeing approved CVM Dec 2015 use –updated SB - June 2016
  Review CVM project against SAE guidelines and determine what has been validated
  Assess FAA rules and determine if adequate for SHM use
Outcome:
  Ensure safe implementation of emerging technologies
  Develop FAA webinar for FAA ACO engineers
  Delta/Boeing investigating further SHM numerous platforms
Comparative Vacuum Monitoring (CVM)
Minimize distance from rivet head to produce smallest crack detection
CVM Sensor
Fatigue Cracks
Monitoring Cracks in B737 Wing Box Fitting

## Slide 6: SAE AISCSHM Committee
Develop standards for SHM for aviation community
ARP6461 “Guidelines for Implementation of Structural Health Monitoring on Fixed Wing Aircraft” published Sept 2013
Probability of Detection area of concern
Reliability workshop April 2015 to determine path forward
Developed 2 POD methodologies for SHM
ARP being developed for POD
Planning a second workshop in 2019
  Develop the test program for validation of the methodologies
  Develop useable data for public use

## Slide 7: Present-Emerging Technologies
To provide SHM capability to the TC Labs:
  Emerging Technologies (Al-Li Panels)
  Wing Box (ABST)
To assess SHM capabilities and collect data
AFT
FWD
Outboard
Inboard

## Slide 8: Full-Scale Aircraft Structural Test Evaluation and Research (FASTER)
History and Background:
Established: Dec. 1998 through partnership with Boeing
•Applies Major Modes of Loading to Fuselage Panels:
–Pressure
–Hoop
–Axial
–Shear

## Slide 9: Baseline Panel Design
74"
125"
20"
7"
76"
Panel Length | 125 inch
Panel Width | 76 inch
Panel Radius | 74 inch
No. of Frames | 6
No. of Stringers | 8
Frame Spacing | 20 inch
Stringer Spacing | 7.0 inch
Skin Thickness | 0.055 inch
Internal View
External View

## Slide 10
Test Matrix – Panels
1
2
3
4
5
 |  | Baseline | Advanced Density Reduction | Advanced Materials | Advanced Materials, FSW | FSW and Bonded Stringers | Baseline MSD | Advanced Density Reduction MSD
Component | Skin | 2524-T3 sheet | 2060 - T8 Al-Li sheet | 2029-T3 sheet | 2029-T3 sheet, FSW | 2060 Al-Li sheet, FSW joint and bonded FML straps | 2524-T3 sheet | 2060 - T8 Al-Li sheet
 | Stringer | 7150 extrusions, riveted | 2055 or 2099 Al-Li extrusions, riveted | 2055 or 2099 Al-Li extrusions, riveted | 2055 or 2099 Al-Li extrusions, FSW | 2055 or 2099 Al-Li extrusions, bonded | 7150 extrusions, riveted | 2055 or 2099 Al-Li extrusions, riveted
 | Frame | 7075-T62 - shear tied, extruded, riveted | 2055 or 2099 Al-Li integral extrusions, riveted | 2055 or 2099 Al-Li integral extrusions, riveted | 2055 or 2099 Al-Li integral extrusions, FSW | 2055 or 2099 Al-Li integral extrusions, riveted | 7075-T62 - shear tied, extruded, riveted | 2055 or 2099 Al-Li integral extrusions, riveted
6
7

## Slide 11: SHM INSTALLED ON PANEL 1

## Slide 12: Airframe Beam Structural Test (ABST) Fixture
Wing skin test panel (24 x 40 in.)

## Slide 13: ABST Test Program
Phase 1: Baseline mechanical and fatigue behavior of
composite panels (pristine and open hole)
Phase 2: Bonded Repair Size Limits
Phase 3 (proposed): Fatigue and DT performance of bonded repairs intentional made deficient to encouraging damage growth
    – Calibrate analysis methods
– Assess NDI and SHM to detect and monitor damage growth

## Slide 14: Phase 1: Panels 1 and 2

## Slide 15: SHM Sensor Layout-PZT

## Slide 16: Future: Reliability
Developed 2 methodologies for POD for SHM
Data from FASTER and ABST tests may be of use to this effort
Working with NASA to develop a model of the FASTER test fixture with SHM
Working with SAE to develop industry std

## Slide 17: Conclusion
Boeing/Delta/AANC met in January 2018 in Seattle to discuss future SHM applications: SB - AD.
SHM: “in situ” NDI. Equal or better. No new guidance needed. Evaluate on case by case basis.
Dual inspections still required when SHM replaces NDI

## Slide 18: Questions
Paul.Swindell@faa.gov
William J Hughes Technical Center
Atlantic City, NJ
609-485-8973