## Slide 2
AA&S Conference , 22-25 May, 2017
Aviation NDT is not like industrial NDT
Aerospace Specific
NDT Training

## Slide 3
AA&S Conference , 22-25 May, 2017
Aerospace Specific
NDT Training
The In-Service Environment
Much more flexible environment than manufacturing
They often see a wide variety of aircraft, old and new
Inspectors are certified in a method, but often use only a few select techniques on a regular basis
Maintenance manual techniques may be confusing and require interpretation
No formalized refresher training

## Slide 4
AA&S Conference , 22-25 May, 2017
Aerospace Specific
NDT Training
420 sites that contained 68 defects
No technician found all the defects
Defects detected ranged from 29% to 71%
Missed cracks ranged in size from 0.058” to 0.286” (3 were over 0.100”) - safety
The false call rate (defect-free areas rejected) was as high as 19.4% - unnecessary maintenance
Performance

## Slide 5
AA&S Conference , 22-25 May, 2017
Aerospace Specific
NDT Training
Average POD is 0.7 mm,
but technicians varied from 0.3 to 0.9 mm
Technician Variability
Variability

## Slide 6
AA&S Conference , 22-25 May, 2017
Reliability Studies
  Sandia PODs – demonstrated the wide variation in technician performance of
  Reliability study –
      best technician found 71% of flaws, lowest performance was 29%
      missed cracks were in the range of 0.058” to 0.0286” (3 were over 0.100”)
      False call rate was 19.4%
  Exam results – only one or two in each class passed, most score in the 40s and 50s.
  These results are not meant to imply that they don’t know what they are doing. But they do emphasize the need for refresher training.
Aerospace Specific
NDT Training

## Slide 7
AA&S Conference , 22-25 May, 2017
Training & Certification
  There are several specifications that govern the training and certification of NDT technicians. NAS-410 is the one that is required by most GA OEMs.
  This covers a vast range of vehicles and environments and as a result, these minimums, while legal, are not intended to be sufficient for a particular vehicle type and environment.
  NDT training providers understandably focus on industrial NDT because that’s where the money is. Commercially available NDT schools do not deal with aerospace and don’t have sufficient specimens for practical exams
Aerospace Specific
NDT Training

## Slide 8
Aerospace Specific
NDT Training
The Need
Relevant Training
Aircraft Design
Static and Dynamic Stresses
Fail Safe / Damage Tolerant Concepts
In-Service Materials Issues (fatigue, corrosion, etc.)
Relevant Practical Exams
Test samples representative of products encountered on the job
Refresher Training

## Slide 9
AA&S Conference , 22-25 May, 2017
Aerospace Specific
NDT Training
In response to these issues (and to meet requirements of NAS-410) Dassault Falcon developed a refresher training program to include:
Aerodynamics, design, stress, fatigue, and corrosion
Emphasis on hands-on work with a wide variety of actual aircraft components
Composite M&P familiarization including specimen fabrication and actual damaged specimens

## Slide 10
AA&S Conference , 22-25 May, 2017
Aerospace Specific
NDT Training
    ET/PT Refresher course, 4 days, once a year
    UT/MT refresher course, 4 days, once a year
    NDT of Composites course, 5 days, twice a year
    Coordination with Structures Engineering
    Establishment of an Aerospace Specimen Library

## Slide 11
AA&S Conference , 22-25 May, 2017
Aerospace Specific
NDT Training
Required of all DFJ shops, independent Authorized Service Centers, and independent NDT providers servicing Falcons
Must attend every three (3) years in each method certified
Since starting program have held 36 classes for approximately 290 students including USAF, RCAF, and RNLAF technicians
Intended to address an engineering issue, not create a training business

## Slide 12
Questions?